## Slide 1
RFID-Enabled Smart Water Dispensing System with Card Control and Live Billing Usage Tracking
Course Title:Internet of Things Lab
Course No: CSE-4264

## Slide 2
Research
participants
Saadman Salman Saad
20210104114
Abdullah Al Maruf
20210104116
Sharun Tawsif
20210104124
Nafisa Tabassum Shouty
20210104127
Group 04
02

## Slide 3
List of Contents
Key Features
Problem Statement
Solution Approach
Project Description
Gap Analysis
Conclusion
System Diagram or Flowchart
List of Required Equipment
Literature Review
03

## Slide 4
Problem Statement
04

## Slide 5
  A smart water dispensing system designed to reduce wastage and ensure fair billing.
  Users authenticate themselves using RFID cards to access water.
  Water flows only while the card is held in place.
  Real-time billing is calculated based on the water used.
  All usage data (volume and cost) is logged automatically to Google Sheets via WiFi.
  Ideal for public water distribution points (e.g., WASA), schools, campuses, or community water stations.
Project Description
04
5

## Slide 6
  ESP32 acts as the central controller with built-in WiFi.
  RFID Reader (RDM6300) reads the user's card and validates it.
  Relay Module activates the Water Pump only while the card is present.
  Billing and volume are calculated using time or flow-based logic.
  LCD Display shows real-time usage and billing info to the user.
  Data is automatically sent to Google Sheets for monitoring and billing logs.
Solution Approach
04
6
How It Works:

## Slide 7
  RFID-Based User Authentication
Only authorized RFID card holders can access the dispenser.
  Smart Water Dispensing
Water flows only while the RFID card is held near the reader.
  Real-Time Usage Monitoring
Tracks how much the water is dispensed
  Live Billing Calculation
Calculates cost based on usage volume.
  LCD Display Feedback
Shows system status, amount used, and bill during operation.
  Automated Data Logging
Sends usage and billing data to Google Sheets via WiFi.
  Power Management
Voltage regulated using buck converter; relay controls high-power pump safely.
  Manual ON/OFF Switch
System can be turned off manually for maintenance or emergencies.
Key Functionalities
04
7

## Slide 8
8
List of Required Equipment

## Slide 9
Project DEtailed Plan
using Flowchart and System Diagram
17

## Slide 10
7. Ready for Next User
  System resets to "Scan RFID Card" for the next user.
  Process repeats.
10
1. System Initialization
  The system powers on via the Power Switch.
  The ESP32 initializes all connected modules:
    RDM6300 RFID Reader
    16x2 LCD Display (via I2C Driver)
    Relay Module
    WiFi Connection Setup
  LCD displays: "Scan RFID Card"
2. User Authentication
  User taps or holds the 125 kHz RFID Card near the RDM6300 reader.
  The ESP32 reads the RFID UID and checks authorization (either from a local list or Firebase/Google Sheets).
  If unauthorized, LCD shows "Access Denied" and resets.
4. Live Usage & Billing
  A timer or flow sensor tracks how long the pump is active (water flow duration).
  The ESP32 calculates:
    Volume used (optional: based on time or flow rate calibration)
    Billing amount (e.g., 1 Litre = X Taka or per second)
  Display updates continuously:
    "Used: 1.25L"
    "Bill: 2.50 TK"
3. Start Water Dispensing
  If the card is valid:
    LCD shows "Access Granted" and starts showing "Water Flowing...".
    ESP32 activates the 5V Relay, turning on the Water Pump.
    Water flows through the Water Pipe from the Water Tank.
5. Stop Dispensing
  When the user removes the RFID card, the ESP32:
    Deactivates the Relay, stopping the Water Pump.
    LCD shows "Dispensing Stopped" and summary of usage.
6. Data Upload to Cloud
  The ESP32 sends the data via WiFi to Google Sheets (using Apps Script + HTTPS or integration platforms like IFTTT or Blynk):
    Card UID
    Time & date
    Amount of water dispensed
    Total charge

## Slide 11
show status, billing
switch ON/OFF
Data sent via WiFi
Google Sheets for billing & usage tracking
Relay Module (1 Channel 5V)
Power Supply
(MP1584 Buck Converter)
16x2 LCD Display +
I2C LCD Driver
Power Switch (manual ON/OFF)
Water Pipe → Water Outlet

## Slide 12
Background Study / Gap Analysis
05
[1] Instructables – Water Dispenser IoT Project
• Components: ESP8266, RFID Module, Relay, LCD, Pump
• Functionality: RFID triggers pump, shows status on LCD, logs via Blynk
• Specialty: DIY-friendly, easy Wi-Fi setup, basic IoT structure
• Gap: No real-time billing or Google Sheets logging; lacks secure ID validation and large-scale tracking
[2] Smart Water ATM (MDPI, Electronics)
• Components: Arduino Uno, RFID Reader, Flow Sensor, Relay, LCD
• Functionality: RFID authentication, flow-based billing, LCD status
• Specialty: Real-time billing with flow rate sensing
• Gap: Does not integrate cloud storage like Google Sheets; lacks Wi-Fi automation for updates
[3] RFID + IoT in Water Vending (ResearchGate)
• Components: NodeMCU, RFID, Ultrasonic Sensor, Relay, GSM
• Functionality: RFID access, tank level sensing, alerts via GSM
• Specialty: Combines IoT + water level + GSM alerts
  Gap: Focus is more on vending control, not detailed billing or usage-based payment tracking
[4] IJARSCT – IoT Water Management for Rural Areas
• Components: Arduino, RFID, Relay, LCD, Pump
• Functionality: RFID access to enable pump, shows info on LCD
• Specialty: Simplicity for low-tech rural deployment
  • Gap: No billing logic or cloud sync; doesn't track individual usage
[5] Academia – Smart Water Dispenser Using RFID
• Components: Arduino, RFID, IR Sensor, LCD, Pump
• Functionality: RFID activates pump; IR detects cup/glass
• Specialty: Safety mechanism for unattended dispensing
• Gap: No billing/tracking system; system is offline only

## Slide 13
Background Study / Gap Analysis
05
[6] GitHub – Smart Water Dispenser System
• Components: ESP32/Arduino, RFID, Ultrasonic Sensor, Relay
• Functionality: RFID for access, tank level sensing, control logic
• Specialty: Open-source and modular design
• Gap: Lacks billing integration and real-time cloud database
[7] IJCRT – Automatic Water Dispenser Using IoT
• Components: RFID, Arduino, Flow Sensor, Pump, Relay
• Functionality: Dispenses water based on flow time
• Specialty: Simple but effective billing logic
• Gap: No RFID-based user logging or data backup via internet
[8] IJARST – Smart Liquid Dispensing Machine
• Components: RFID, Solenoid Valve, Arduino, LCD
• Functionality: Dispenses set amount after authentication
• Specialty: Precise, fixed-volume dispensing system
• Gap: Does not measure actual usage; lacks billing customization and tracking
[9] IJIRT – Automatic Water Dispenser Using IoT
• Components: Arduino, RFID, Solenoid Valve, Relay, LCD
• Functionality: Dispenses a predefined quantity on RFID scan
• Specialty: Fixed pricing model for community water supply
• Gap: No cloud integration; does not allow dynamic billing based on use
[10] Smart Water Dispenser Monitoring System (Conf. Proc.)
• Components: RFID, Ultrasonic Sensor, WiFi Module, Relay
• Functionality: RFID-based access + water level monitor
• Specialty: Adds monitoring analytics
• Gap: No detailed user billing or integration with billing APIs like Google Sheets

## Slide 14
Conclusion
14
28
The RFID-enabled Smart Water Dispensing System offers an innovative, efficient, and accountable solution to modern water distribution challenges. By integrating IoT, automation, and real-time billing, it ensures fair usage, prevents wastage, and promotes digital water management. This system can significantly contribute to sustainable water practices in both urban and rural areas.

## Slide 15
Reference
29
[6] A. Labrahmi, “Arduino Smart Water Dispenser System,” GitHub Project Repository, 2022. [Online]. Available: https://github.com/Labrahmi/water-dispenser-system
[1] Instructables Team, “Water Dispenser IoT Project,” Instructables, 2024. [Online]. Available: https://www.instructables.com/Water-Dispenser/
[2] K. Abubakar, M. Tariq, and S. R. Ali, “Smart Water ATM with Arduino Integration, RFID Authentication, and Dynamic Dispensing,” Electronics, vol. 13, no. 9, p. 1657, 2024. [Online]. Available: https://www.mdpi.com/2079-9292/13/9/1657
[4] P. Kumari and R. Sinha, “IoT Based Water Management System using RFID for Rural Areas,” International Journal of Advanced Research in Science, Communication and Technology (IJARSCT), vol. 4, no. 5, pp. 123–130, 2024. [Online]. Available: https://ijarsct.co.in/A16820.pdf
[5] N. Jaiswal and R. Jaiswal, “Smart Water Dispenser Using RFID Reader,” Project Report, Academia.edu, 2023. [Online]. Available: https://www.academia.edu/42654070
[3] H. Ahmed, “Advancing Water Vending Industry through RFID and IoT Empowerment,” International Conference on Advanced Electrical and Electronics Engineering (ICAEEE), 2024. [Online]. Available: https://www.researchgate.net/publication/381693362

## Slide 16
Reference
30
[7] S. Jain, M. Yadav, and D. Kumar, “Automatic Water Dispenser Using IoT,” International Journal of Creative Research Thoughts (IJCRT), vol. 12, no. 4, pp. 88–91, 2024. [Online]. Available: https://ijcrt.org/papers/IJCRT24A3196.pdf
[8] V. K. Singh, “Design and Construction of a Smart Liquid Dispensing Machine,” International Journal of Advanced Research in Science and Technology (IJARST), vol. 9, no. 2, pp. 55–60, 2023. [Online]. Available: https://www.ijarst.in/public/uploads/paper/951851654145888.pdf
[9] A. Patel, R. Bhatt, and S. Shah, “Automatic Water Dispenser Using IoT,” International Journal of Innovative Research in Technology (IJIRT), vol. 11, no. 3, pp. 112–117, 2024. [Online]. Available: https://ijirt.org/publishedpaper/IJIRT164235_PAPER.pdf
[10] R. Deshmukh and P. Joshi, “Smart Water Dispenser Monitoring System,” International Conference Proceedings on Embedded and IoT Systems, 2020.

## Slide 17
ANY
Question?